## Slide 1
ACTIVITY IDENTIFICATION
FROM ANIMAL GPS TRACKS
With Spatial Temporal Clustering Method
DDB-SMoT
Master’s Thesis Defense
Simiao Sun
Advisor: Dr. Yi Shang

## Slide 2: Overview
Introduction
Related Work
Methodology
Experiment
Summary and Future Work

## Slide 3: Animal GPS Tracks

## Slide 4: Infer Animal Activity from GPS Tracks
Current Condition:
  Lots of GPS devices provide us with huge amount of wildlife GPS data
  GPS data does not directly improve semantic richness
    Still have no information about the meaning of the GPS data
  Need to associate GPS data with the real world
Problem:
  How to solve the semantic gap between raw GPS data and the real world

## Slide 5: Motivation
Wildlife semantic data is more useful than raw GPS data
  Better control the animal population
  Better protection for animal
  Better understanding of animals
Find a way to fill the semantic gaps
  Large amount of GPS tracks
  Lack of wildlife semantic data

## Slide 6: Problem Definition
Data Source: Missouri Black Bear/Deer GPS data
  T = [P1,P2,…Pn]
  Pi = [lon, lat, timestamp]
Method:
  POI(Point of Interest)
  Stop Detection Algorithm: Direction and Distance Based- Stop and Move of Trajectory (DDB-SMoT)
  Probability Model: Inverse-square Laws
Purpose: predict the activities that animals performed in the trajectory
  Bear1001: mating  drinking  …

## Slide 7: Thesis Achievements
DDB-SMoT
  A new stops detection algorithm based on DB-SMoT
Semantic Analysis Software
  A software to predict a list of activities performed given an input of animal trajectory and POI dataset
Semantic Analysis Web Application
  A web application to display the semantic enrichment result
Animal Trajectory Generator
  A software to generate trajectories that are similar to real animal trajectory

## Slide 8: Overview
Introduction
Related Work
Methodology
Experiment
Summary and Future Work

## Slide 9: Semantic Analysis Related Work
Previously, more related works have been done for analyzing human GPS tracks
Two main trends for related works:
  Trend 1: Concentrate on transportation means identification
    Yu Zheng, Like Liu, Longhao Wang, and Xing Xie. “Learning transportation mode from raw GPS data for geographic applications on the web.” In WWW, pages 247–256, 2008.
  Trend 2: Focus on inferring human activities
    Arbara Furletti, Paolo Cintia, and Chiara Renso. “Inferring human activities from GPS tracks.” Chicago, USA, 2013. ACM.

## Slide 10: Semantic Analysis Related Work
Previous works provide us with two approaches:
  Approach 1:
    Use Spatial Temporal POI’s Attractiveness (STPA) to identify activity-locations and durations
    Use POI to match trajectories
    Very detailed geographic information needed
      Fame, Size of each POI
  Approach 2:
    Use stops in the trajectories to match visited POIs and then infer the corresponding activities
    Use stops to match POIs

## Slide 11: Stops Detection Related Work
There are mainly three types of GPS stops detection algorithms :
  IB-SMoT: Intersection Based – Stop and Move of Trajectory
  CB-SMoT: Clustering Based – Stop and Move of Trajectory
  DB-SMoT: Direction Based – Stop and Move of Trajectory
IB-SMoT and CB-SMoT:
  Choose stops matches important places in application
  Trajectory should stay in a fixed area
DB-SMoT better fits our condition

## Slide 12: Overview
Introduction
Related Work
Methodology
Experiment
Summary and Future Work

## Slide 13: Semantic Enrichment Process

## Slide 14: 1. Stops Detection
Stops detection algorithm DDB-SMoT
  Input: T[P1,P2…Pn], MinDirChange, MaxDisChange, MaxTimeChange, MinTime, MaxTol
  Output: a list of stops and moves
O(n) Time Complexity
Require very dense GPS data
Use only direction change between each two points
O(n) Time Complexity
Can apply to both dense and sparse GPS data
Consider direction change, distance and timestamp between each two points
DB-SMoT
DDB-SMoT

## Slide 15: 1. Stops Detection Definitions
Basic definitions for DDB-SMoT in trajectory T[P1,P2…Pn]
  Direction Change: Angle of direction Pi-1Pi and direction PiPi+1
    MinDirChange
  Distance Change: Distance between Pi-1 and Pi
    MaxDisChange
  Time Change (Optional): Time difference between Pi-1 and Pi
    MaxTimeChange
  Time Duration: The time that the animal stays at the stop
    MinTime
  Tolerance: The number of trajectory points with
  Dirchange < MinDirChange that can be found
  consecutively in a stop cluster
    MaxTol
Pi-1
Pi
Pi+1
DirChange
DisChange

## Slide 16: 1. Stops Detection Example
P1
P2
P3
P4
P5
P6
P7
P8
P9
P2, P3 : DirChange>MinDirChange
P4 : DirChange<MinDirChange
P5, P6 : DirChange>MinDirChange
P7, P8, : DirChange<MinDirChange
Result: Stop cluster [P1,P2,P3,P4,P5,P6]
75
450
600
400
350
240
400
375
MaxTol: 1
MaxDisChange:500m
MinDirChange:90o
MinTime:2 hours
Result: Stop cluster [P1,P2,P3,P4,P5]
MaxTimeChange: 24 hours

## Slide 17: 2. Associate Stops with POIs
Stops can be detected by DDB-SMoT
Stop should be associated with POIs
  POI(Lon, Lat, Category)
  The Category above will map to an Activity, eg. RiverDrinking. (An Activity will have multiple Categories)
Select POI that satisfies these two requirements
  If POI is reachable
    dis(POI, Stop) < MaxReachDistance
  If the available time of POI intersects the stop time duration
    We don’t have this information yet

## Slide 18: 3. Infer Activity from POIs
Use probability model(derived from Inverse-square Law) to determine the probability(P) of an activity(act) for a stop(s):
  Inverse-square Law: mass1*mass2/(distance2)
  (mass1 will always be 1, mass2 will be the number of POIs from selected POIs related to the same activity)
Choose the Max(P(s,act)) to infer the activity

## Slide 19: 3. Infer Activity from POIs
S
POI1
POI4
POI3
POI2
POI6
POI5
60
75
110
70
50
75
Act1: POI1, POI2, POI3
Act2: POI4, POI6
Act3: POI5
P(S,Act1) = 1×3/602×Φ = 0.36
P(S,Act2) = 1×2/502×Φ = 0.52
P(S,Act3) = 1×1/752×Φ = 0.12
 Perform Act2 at S

## Slide 20: Animal Trajectory Generator
Stops detection affects the accuracy of the result
  Need a platform to verify the stops detection algorithm
Trajectory Generator provides with labeled trajectories that are similar to the real animal trajectory
Prepare POIs
Generate points towards or around a POI
Terminate
Stop Model
Movement Model
Start
No more POI left
Has more POI left

## Slide 21: State Transition Model
Stop
Move
p: current point’s label
p.n: next point’s label
s: stop label
m: move label
P(p.n=m | p=s)
P(p.n=s | p=s)
Dis(p,POI)>POI.radius
Dis(p,POI)<=POI.radius

## Slide 22: Movement Model
Assumption: Purpose of Movement is to get closer to the POI and get into the Stop Model
Parameters for the model:
  Distance Change (dis)
  Direction Change (dirchange)
Choose from Pnext and Pnext’
Make sure dis(Pnext,POI)<dis(Pcur,POI)
Ppre
Pcur
Pnext
d1
θ
Pnext’
θ
d1 = dis θ = dirchange
POI
d2
d1

## Slide 23: Movement Model
Generate the next point:
Based on the formula of angle between directions:
Based on the distance between
current and next point:
Choose from Pnext and Pnext’
Make sure dis(Pnext,POI)<dis(Pcur,POI)
Ppre
Pcur
Pnext
d1
θ
Pnext’
θ
d1 = dis θ = dirchange
POI
d2
d1
Ppre(xp,yp)
Pcur(xc,yc)
Pnext(xn,yn)

## Slide 24: Stop Model
Assumption: Purpose of Stop is to stay inside the POI range to perform activity
Parameters for the model:
  Distance Change (dis)
  Direction Change (dirchange)
Choose from Pnext and Pnext’
Make sure dis(Pnext,POI)<POI.radius
Ppre
Pcur
Pnext
d1
θ
Pnext’
θ
POI
d2
d1
POI.radius
d1 = dis θ = dirchange

## Slide 25: Overview
Introduction
Related Work
Methodology
Experiment
Summary and Future Work

## Slide 26: Experiment Dataset
Missouri Black Bear GPS Data
  Total num of bear: 78
  110000 GPS points
Missouri Deer GPS Data
  Total num of deer: 114
  150000 GPS points
Trajectories similar to Missouri black bear trajectory
  Generated by Animal Trajectory Generator
  Features extracted from Missouri black bear GPS data

## Slide 27: Experiments
Performance evaluation for DDB-SMoT
  Use trajectories provided by Animal Trajectory Generator
  Features extracted from black bear trajectory
  Compare accuracy with DB-SMoT
Semantic Analysis Experiments
  Use Missouri black bear and deer GPS data

## Slide 28: DDB-SMoT Performance Evaluation
Use labeled trajectory
Apply DDB-SMoT
  Label each point with prediction result
Evaluate the accuracy of the stops detection algorithm from three bench marks:
  Stop points accuracy
  Move points accuracy
  Overall accuracy

## Slide 29: DDB-SMoT Performance Evaluation

## Slide 30: DDB-SMoT Performance Evaluation

## Slide 31: DDB-SMoT Performance Evaluation
Compare with DB-SMoT:
  Better overall accuracy
  Largely improved move points accuracy
  Stop points accuracy around the same

## Slide 32: Semantic Analysis Experiments
Currently, no accuracy of semantic analysis can be calculated
  POI dataset not available
  No ground truth labeled with the GPS points
Semantic analysis web application
  Visualize the whole semantic enrichment process
  Semantic analysis for black bear and deer GPS data

## Slide 33: Semantic Analysis Experiments

## Slide 34: Semantic Analysis Experiments
Before Stops Detection
After Stops Detection

## Slide 35: Semantic Analysis Experiments

## Slide 36: Overview
Introduction
Related Work
Methodology
Experiment
Summary and Future Work

## Slide 37: Summary
New stops detection algorithm DDB-SMoT
  More accurate than DB-SMoT
Semantic Analysis Software
  Lack of rich POI data, cannot provide real prediction
  Lack of ground truth from observation, cannot calculate accuracy
Semantic Analysis Web Application
  Available for visualizing the semantic enrichment process
Animal Trajectory Generator
  Can be used for generating trajectories similar to animal GPS tracks

## Slide 38: Future Work
Revise semantic analysis model
  The network of animals can be taken into consideration
  Multiple activities may happen in the same place
Build the POI dataset:
  Use stops detection result as a reference to find POIs near stops
Evaluate semantic enrichment process

## Slide 39
Thanks For Presences
Questions ?